## Slide 1: COSC 290 (Lab) #6
Amaizu Gabriel
gamaizu1@students.towson.edu
Notes: 원진킴

## Slide 2: Basic Micro Computer Design
Central Processor Unit (CPU)
registers
CU
Clock
ALU
Memory Storage Unit
I/O Device #1
I/O Device #2
data bus, I/O bus
address bus
control bus

## Slide 3: Combinational Logic Circuit
Definition
  A circuit that its output is depended only on the inputs at the same instant of time
Combinational Logic Circuit
input
output

## Slide 4: Sequential Logic Circuit
Definition
  A circuit that its output depends not only on the given inputs but also on the past history of inputs
Memory
Binary info
Clock Signal
Combinational Logic Circuit
input
output

## Slide 5: Sequential Logic Circuit (cont)
  Memory Storage
    Latch
      Operated when the clock is active (i.e. clock = 1)  Not synchronized within the computer system!
    Flip-Flop
      Operated only at the edges (rising or falling) of the clock

## Slide 6: Difference between latch and Flip-Flops
Output waveform of Latch
Output waveform of JK Flip-Flops

## Slide 7: SR Latch
Set-Reset latch circuit diagram (1)
NOR SR latch’s characteristic table |  | 
S | R | Action
0 | 0 | No change
0 | 1 | Q = 0 (reset)
1 | 0 | Q = 1 (set)
1 | 1 | Forbidden

## Slide 8: SR Latch (cont)
Set-Reset latch circuit diagram (2)
NAND SR latch’s characteristic table |  | 
 |  | Action
0 | 0 | Forbidden
0 | 1 | Q = 1 (set)
1 | 0 | Q = 0 (reset)
1 | 1 | No change
NAND SR latch’s characteristic table |  | 
 |  | Action
0 | 0 | Forbidden
0 | 1 | Q = 1 (set)
1 | 0 | Q = 0 (reset)
1 | 1 | No change

## Slide 9: SR Flip-Flop
Set-Reset flip-flop circuit diagram
SR FF’s characteristic table |  | 
S | R | Action
0 | 0 | No change
0 | 1 | Q = 0 (reset)
1 | 0 | Q = 1 (set)
1 | 1 | Invalid

## Slide 10: D Flip-Flop
Description
  Data (or Delay) Flip-Flop
D FF’s characteristic table | 
D | Action (
0 | 0 (reset)
1 | 1 (set)
D FF’s characteristic table | 
D | 
0 | 0 (reset)
1 | 1 (set)

## Slide 11: JK Flip-Flop
Description
  Another alternative of SR FF
JK FF’s characteristic table |  | 
J(set) | K(reset) | Action ()
0 | 0 | 
0 | 1 | Q = 0 (reset)
1 | 0 | Q = 1 (set)
1 | 1 | (toggle)
JK FF’s characteristic table |  | 
J(set) | K(reset) | 
0 | 0 | 
0 | 1 | Q = 0 (reset)
1 | 0 | Q = 1 (set)
1 | 1 | 

## Slide 12: T Flip-Flop
Description
  Trigger-Flip-Flop using SR Latch
  Operated only when trigger is on
T | Q | Qnext | Comment
0 | 0 | 0 | Hold state
0 | 1 | 1 | Hold state
1 | 0 | 1 | Toggle
1 | 1 | 0 | Toggle