## Slide 1: Wireless Networking Technologies

## Slide 2: Taxonomy of wireless networking technologies
Wireless networks
  LAN
  MAN
  WAN
  PAN
  WSN (sensor networks)
  Cellular Networks
  Ad-Hoc Networks

## Slide 3: Personal Area Networks (PANs)
Intended for a single user
  Bluetooth:
    short distance comm. between small devices
  InfraRed:
    line-of-sight required, between small devices
  ZigBee:
    ZigBee is the only open, global wireless standard to provide the foundation for the Internet of Things by enabling simple and smart objects to work together
  UWB (Ultra-wide band)
    PC peripherals, radar, imaging
  ISM wireless:
    frequencies set aside for Industrial, Scientific and Medical devices, 3 ranges of freq.

## Slide 4: ISM Wireless Bands Used by LANs and PANs
A region of electromagnetic spectrum is reserved for use by Industrial, Scientific, and Medical (ISM) groups
  Known as ISM wireless
Not licensed to specific carriers
  available for LANs and PANs
Figure 16.3 (below) illustrates the ISM frequency ranges

## Slide 5: Wireless LAN Technologies and Wi-Fi
A variety of wireless LAN technologies utilizing:
  frequencies
  modulation techniques
  data rates
Standardized by IEEE as IEEE 802.11
Wi-Fi Alliance
  a non-profit organization that tests and certifies wireless equipment using the 802.11 standards

## Slide 6: Key wireless standards
IEEE standard | Frequency Band | Data Rate | Modulation and multiplexing techniques
Original 802.11 | 2.4GHz | 1 or 2 Mbps | DSSS, FHSS
 | 2.4GHz | 1 or 2 Mbps | FHSS
 | Infrared | 1 or 2 Mbps | PPM
802.11b | 2.4GHz | 5.5 to 11 Mbps | DSSS
802.11g | 2.4GHz | 22 to 54 Mbps | OFDM, DSSS
802.11n | 2.4GHz | 54 to 600 Mbps | OFDM

## Slide 7: Spread Spectrum Techniques
Spread spectrum
  the sender spreads data across multiple frequencies
  the receiver combines the information obtained from multiple frequencies to reproduce the original data
Goals
  Increase overall performance
  Make transmission more immune to noise
The three key multiplexing techniques used in Wi-Fi wireless networks
  FHSS
  DSSS
  OFDM

## Slide 9: Other wireless standards
802.11e: improved QoS – low jitter
802.11i: enhanced security
802.11k: radio source management
802.11n: data rate over 100Mbps (multimedia)
802.11p: comm. Among vehicles on a highway
802.11r: improved roaming capability
802.11s: proposed for mesh network
802.11ac: use of 5GHz band. Max single link of 500megabits (up to 256 QAM)
802.11ad: “WiGig” use of 60GHz, up to 7Gbps
  “microwave Wi-Fi”, ranges from 1 to 10 meters
IEEE 802.11ah and 802.11af, runs at just 900MHz and will offer very poor data speeds, but works across huge areas. While WiGig will supercharge homes, it's IEEE 802.11ah that will fuel what should probably be renamed the Wi-Fi Internet of Everything

## Slide 10
Standard | Frequency Band | Max Speed | Main Features | Use Cases
802.11ax (Wi-Fi 6/6E) - 2019 | 2.4 GHz, 5 GHz, 6 GHz (6E) | 9.6 Gbps | OFDMA, MU-MIMO, 1024-QAM, BSS Coloring, TWT | IoT, smart homes, high-density environments
802.11be (Wi-Fi 7) | 2.4 GHz, 5 GHz, 6 GHz | 46 Gbps (theoretical) | 320 MHz channels, 4K-QAM, Multi-Link Operation | AR/VR, 8K streaming, enterprise environments
802.11ad (WiGig) | 60 GHz | 7 Gbps | High-speed, short-range, ideal for point-to-point communication | Wireless VR, HD media streaming, docking stations
802.11ay | 60 GHz | 176 Gbps (theoretical) | Enhanced range and speed over 802.11ad | 8K streaming, wireless data centers, VR
802.11ah (HaLow) | Sub-1 GHz (900 MHz) | 347 Mbps | Low power, long-range, IoT-focused | IoT, smart cities, industrial automation
802.11af (White-Fi) | TV White Spaces | 568 Mbps | Long-range, uses TV broadcast frequencies | Rural broadband, smart agriculture, IoT
Summary of Key Wi-Fi Standards:

## Slide 11: Wireless LAN architecture
The three building blocks:
  Access points (AP) – base station
  An interconnection mechanism
  A set of wireless hosts
two types of wireless LANs are possible:
  Ad hoc
  Infrastructure based
Application: AP throughout buildings

## Slide 12
Basic service set

## Slide 13: Overlap, Association, and 802.11 Frame Format
More than one access point – overlap
Area not covered by any access point – deadzone
Associate with only one access point
For internet access – needs router’s MAC address
CTL: Frame control (protocol version, type, etc)
DUR: Duration ID

## Slide 14
Handoff from weaker signal strength to stronger signal

## Slide 15: Contention and Contention-Free Access
The original 802.11 standard defined two general approaches for channel access
  Point Coordinated Function (PCF)
  Distributed Coordinated Function (DCF) for contention-based service
    BSS uses a random access protocol
Hidden station problem
802.11 networks use CSMA/CA
  Exchange RTS and CTS messages before transmission

## Slide 16: Contention and Contention-Free Access
The 802.11 standard defines three timing parameters as follows:
Short Inter-Frame Space (SIFS) of 10 (or 16 in 11n and 11ac) µsec
  Time to wait before sending an ACK or other response
Distributed Inter-Frame Space (DIFS) of 50 (or 34 in 11n and 11ac) µsec
  Time to idle before a station can attempt transmission
  2 slot time plus SIFS
Slot Time of 20 (or 9 in 11a, 11n, 11ac) µsec

## Slide 18: Wireless MAN tech and WiMax
IEEE standard 802.16
  Fixed WiMAX – informally 802.16d
    Doesn’t provide handoff among APs (service to a fixed location)
  Mobile WiMAX – 802.16e-2005
Potential Usage
  access
    Last mile alternative to DSL or cable modem
    As a backup for a site’s Internet connection
  interconnect
    Backhaul (conn. Between a service provider and remote cell tower)
    Private connection (multiple sites of a company)
    Connection between small and large ISPs
Comparison between WiMax and LTE
  WiMAX: low cost, 4G based on the IEEE 802.16, largely overtaken by LTE and 5G
  LTE-A: backward compatible, true 4G technology (max of 1Gbps)

## Slide 19: Wireless MAN Technology and WiMax
(Non-line-of-sight)
WiMax, LTE, 5G or MIMO

## Slide 20: Wireless MAN Technology and WiMax
The key features of WiMAX can be summarized as follows:
  Uses licensed spectrum (i.e., offered by carriers)
  Each cell can cover a radius of 3 to 10 Km
  Uses scalable orthogonal FDM
  Guarantees quality of services (for voice or video)
  Can transport 70 Mbps in each direction at short distances
  Provides 10 Mbps over a long distance (10 Km)

## Slide 21: PAN tech and Standards
IEEE has assigned the number 802.15 to PAN standards
  802.15.1a: Bluetooth (1Mbps, 2.4GHz)
  802.15.2-2003: coexistance among WPANs – task group went into “hibernation”
  802.15.3: High rate PAN (55Mbps, 2.4GHz)
  802.15.3a: Ultra Wideband(UWB) (110Mbps, 2.4GHz)
  802.15.4: Zigbee tech – low data rate for remote
  802.15.4a: alternative – low power

## Slide 22: PAN tech and Standards cont’
Bluetooth
  Short distance – usually up to 5 meters
  Device is master or slave
  Master grants permission to slave
  Data rate is up to 721Kbps
UWB (Ultra-wide band) – PC peripherals, radar, imaging
  Wide spectrum of frequencies
  Short distance (2 to 10 meters)
  Data rate 110Mbps at 10 meters, up to 500 at 2 meters

## Slide 23: PAN tech and Standards cont’
Zigbee
  Wireless standard for remote control, not data
  Industry/home automation
  3 frequencies (868 MHz, 915 MHz, and 2.4 GHz)
  Data rate 20, 40, 250Kbps
  Low power consumption
  Three levels of security

## Slide 24: Other Short Distance Comm. Tech.
InfraRED – wavelength longer than visible light
  The Infrared data association (IrDA) has a set of standards
    Data rates between 2.4Kbps(control) and 16Mbps(data)
    Range of 1 to several meters
  Military: target acquisition, surveillance, night vision
  Civilian: remote temperature sensing, remote control

## Slide 25: Other Short Distance Comm. Tech. cont’
Radio Frequency Identification (RFID) - A small tag contains ID info and a receiver can “pull” from the tag
  Over 140 RFID standards exist
  Passive RFID draw power from the signal sent by the reader
  Uses frequencies from less than 100MHz to 868-954MHz
  Uses for inventory, sensors, passports, etc

## Slide 26: Other Short Distance Comm. Tech. cont’
Radio Frequency Identification (RFID)
  A small tag contains identification information
Some features of RFID:
  Over 140 RFID standards exist for a variety of applications
  Passive RFIDs draw power from the signal sent by the reader
  Active RFIDs contain a battery (last up to 10 years)
  Limited distance
    Passive: 2ft ~ 20ft
    Active : up to 1500ft
  Frequencies from less than 100 MHz to 868-954 MHz
  Used for inventory control, sensors, passports, and other applications

## Slide 27: Wireless WAN Technologies
Wireless WAN technologies can be divided into two categories:
  Cellular communication systems
  Satellite communication systems

## Slide 28: Wireless WAN Technologies - Cellular Communication Systems
voice services to mobile customers
  interconnect cells to the public telephone
cellular systems provide data services and Internet connectivity
In terms of architecture
  each cell contains a tower
  a group of (usually adjacent) cells is connected to a Mobile Switching Center (MSC)
The center tracks a mobile user
  manages handoff

## Slide 29: Cellular Communication Systems

## Slide 30: Cellular Communication Systems
Perfect cellular coverage occurs if each cell is a hexagon
  the cells can be arranged in a honeycomb
  In practice, cellular coverage is imperfect
Most cell towers use omnidirectional antennas
  transmit in a circular pattern
  obstructions and electrical interference can attenuate a signal or cause an irregular pattern

## Slide 31
Variability in cell density (urban, rural setting)

## Slide 32: Cell Clusters and Frequency Reuse
Cellular communication follows a key principle:
  an adjacent pair of cells do not use the same frequency
To implement the principle
  A cluster approach
    a small pattern of cells
clusters of size 3, 4, 7, and 12 that are commonly used

## Slide 33: Cell Clusters and Frequency Reuse
Clusters can cover an entire area without leaving any gaps
each cell is assigned a unique frequency
  adjacent cells will not have the same frequency
Figure 16.17 illustrates a replication of the 7-cell cluster

## Slide 35: Generations of Cellular Technologies
Four generations in cellular technologies
  1G, 2G, 3G, 4G, and 5G
  intermediate versions: 2.5G and 3.5G
1G
  Began in the late 1970s, and extended through the 1980s
  Originally called cellular mobile radio telephones
    used analog signals to carry voice
2G and 2.5G
  Began in the early 1990s and continues to be used
  2G uses digital signals to carry voice
  2.5G
    some 3G features

## Slide 36: Generations of Cellular Technologies
3G and 3.5G
  Began in the 2000s
  higher-speed data services
  download rates of 400 Kbps to 2 Mbps,
    web browsing and photo sharing
  roam across the world
4G
  Began around 2008 – “IMT-Advanced” by ITU-R
  Support for real-time multimedia
  100Mbps while moving rapidly, 1Gbps while moving slowly
  All-IP based mobile broadband
  multiple connection technologies
    Wi-Fi and satellite
5G
  Peak data rate of 10Gbps but typically 100Mbps and 1 Gbps
  Low latency – under 1 millisecond
  Support 100 times more devices per square kilometer than 4G
  Network slicing

## Slide 37: Generations of Cellular Technologies
A variety of standards have evolved
  The European Conference of Postal and Telecommunications Administrators selected Global System for Mobile Communications (GSM)
  Motorola invented a TDMA system known as iDEN
  Most US and Asian carriers adopted a CDMA approach that was standardized as IS-95A
  Japan created a TDMA technology known as PDC (personal digital cellular)

## Slide 38
Approach/classification | Standard
GSM (a TDMA technology) | GSM, FPRS, EDGE, EDGE Evolution, HSCSD
CDMA | IS-95A, IS-95B (extended to produce CDMA2000)
TDMA | iDEN, IS-136, POC (push-to-talk over cellular)
WCDMA | UMTS, HSDPA
Can be advertised as 4G | HSPA+, HTC EVO 4G, WiMAX
Adheres to IMT-Advanced | LTE Advanced, WiMAX advanced
4th generation cellular wireless standards

## Slide 39: Generations of Cellular Technologies
Basic communication mechanism
  General Packet Radio Service (GPRS) for Internet access
    For 2G and 3G GSM, packet oriented best effort, 56-114 kbps
  Short Message Service (SMS) is used for texting
  Wireless Application Service (WAP) is used to access Internet
    WAP browser for cell phones, email, stocks, sports, etc
  Multimedia Messaging service (MMS) is used for multi-media
GPRS technologies evolved further (higher data rate):
  Enhanced Data rate for GSM Evolution (EDGE)
    known as Enhanced GPRS (EGPRS)
    EDGE Evolution, 236.8 kbps
    For any packet switched application

## Slide 40: Generations of Cellular Technologies
Interoperability
  A few key standards from 2G
  IS-136, PDC, IS-95A, and EDGE all influenced the design of UMTS, a technology that uses Wideband CDMA (WCDMA)
  IS-95B was extended to produce CDMA 2000
Standards for 3G data services
  EVDO (Evolution Data Optimized or Evolution Data Only) and EVDV
    Combined CDMA and FDM
  High-Speed Downlink Packet Access (HSDPA) offers download speeds of 14 Mbps

## Slide 41: VSAT Satellite Technology
The key to satellite communication is a parabolic dish antenna
  Very Small Aperture Terminal (VSAT) allows two-way satellite communication (mostly 75cm ~ 1.2m)
  Electromagnetic energy arriving from a distant satellite is reflected to a single focus point
  By aiming the dish at a satellite (geosynchronous) and placing a detector at the focus point

## Slide 43: VSAT Satellite Technology
VSAT satellites use three frequency ranges that differ in
  the strength of the signal delivered
  the sensitivity to rain and other atmospheric conditions
  the area of the earth's surface covered (satellite's footprint)

## Slide 44: GPS Satellites
Global Positioning System (GPS)
  Navigation, location-based services (LBS) for POI
The key features are:
  Accuracy between 2-20 meters
  24 total satellites orbit the earth
  Satellites arranged in six (6) orbital planes
  Provides time synchronization
Obtaining position information
  All GPS satellites orbit in well-known positions
    Use the distance to three satellites
NAVSTAR GPS satellite

## Slide 45: Software Radio and the Future of Wireless
Special-purpose radio hardware
  The antenna, transmitter, and receiver in a given device using predetermined frequencies
A cell phone with GSM, Wi-Fi, and CDMA
  Must have three completely separate radio systems
Traditional radios are being replaced by radios that follow a programmable paradigm
  Features are controlled by software running on a processor

## Slide 46: Software Radio and the Future of Wireless

## Slide 47: Software Radio and the Future of Wireless
The key technologies:
  Tunable analog filters and multiple antenna management
    Analog chips -> tunable analog filters
  Digital Signal Processors (DSPs)
  Multiple-Input Multiple-Output (MIMO)
    multiple antennas for both transmission and reception => spatial multiplexing
  Universal Software Radio Peripheral (USRP) and GNU Radio
    Uses software defined components such as mixers, filters, amplifiers, modulators/demodulators, detectors, etc.