## Slide 1: Reliability and Channel Coding

## Slide 2: Transmission Errors
  External electromagnetic signals can cause incorrect delivery of data
    Data can be received incorrectly
    Data can be lost
    Unwanted data can be generated
  Any of these problems are called transmission errors
  Three main sources of transmission errors
    Interference
    Distortion
    Attenuation

## Slide 3: The main sources - Interference
Electromagnetic radiation – electric motors
background cosmic radiation – natural environment
Can disturb radio transmissions and signals traveling across wires

## Slide 4: The main sources - Distortion
All physical systems distort signals
As a pulse travels along an optical fiber, the pulse disperses
Wires have properties of capacitance and inductance
large metal object affect the set of passable frequencies - can block some frequencies of radio waves

## Slide 5: The main sources - Attenuation
As a signal passes across a medium, the signal becomes weaker
  Signals become weaker over long distances

## Slide 6: Approaches to reduce errors
Shannon's Theorem:
  increase the signal-to-noise ratio
    By increasing the signal or
    By lowering noise
Shielded wiring
Noise/interference cannot be eliminated completely
  transmission errors can be detected
  Some errors can be corrected automatically
Error detection adds overhead
Error handling is a tradeoff, system designers
  must decide whether a given error is likely to occur
  Analyze the consequences

## Slide 7: Effect of Transmission errors on data
Single bit error: often caused by very short-duration interference
Burst Error: multiple bits in a block of bits are changed – often caused by long-duration interference
Erasure (ambiguity): does not clearly correspond to either a logical 1 or a logical 0 – often caused by distortion or interference

## Slide 8: Effect or Transmission errors on data cont’
For a burst error, the burst size, or length, is defined as the number of bits from the start of the corruption to the end of the corruption
Figure 8.2 illustrates the definition

## Slide 9: Two Strategies for Handling Channel Errors
Channel Coding
  mathematical techniques designed to overcome errors during transmission and increase reliability
Two broad categories:
  Forward Error Correction (FEC) mechanisms
  Automatic Repeat reQuest (ARQ) mechanisms
The basic idea of FEC
  add additional information to data to verify that data arrives correctly and to correct errors, if possible

## Slide 10: Two Strategies for Handling Channel Errors cont’

## Slide 11: Block and Convolutional Error Codes
The two types of FEC techniques satisfy separate needs:
Block Error Codes
  It divides the data to be sent into a set of blocks
  It attaches redundancy to each block
  the encoding mechanism does not carry state information across blocks -> no memory required
Convolutional Error Codes
  It treats data as a series of bits, and computes a code over a continuous series
  the code computed for a set of bits depends on
    the current input and some of the previous bits in the stream
  Convolutional codes need memory

## Slide 12: Error detection and correction
Error detection –
  Send additional information so incorrect data can be detected and rejected (Automatic Repeat reQuest (ARQ) mechanism)
  Determine changed bits exactly and to compute correct values
Error correction –
  Send additional information so incorrect data can be corrected and accepted ( Forward Error Correction (FEC) mechanism)
  Sender and receiver exchange messages to insure that all data arrives correctly

## Slide 13: Parity checking
  Parity refers to the number of bits set to 1 in the data item
    Even parity - an even number of bits are 1
    Odd parity - an odd number of bits are 1
  A parity bit is an extra bit transmitted with a data item, chose to give the resulting bits even or odd parity

## Slide 14: Example

## Slide 15: The Mathematics of Block Error Codes and (n, k) Notation
Mathematically
  we define the set of all possible messages to be a set of datawords -> k
  and define the set of all possible encoded versions to be a set of codewords -> n
(n, k) encoding scheme
  where n = k + r, r is additional bits
Error detection utilizes 2 valid codewords
  The valid subset is known as a codebook

## Slide 16: Example: Valid codewords
Consider 3 bit data with even parity
n = k + r = 3 + 1
      0000
      0011
      0101
      0110
      1001
      1010
      1100
      1111
out of 16 possible codewords, only 8 is valid

## Slide 17: Hamming Distance
Given two strings of n bits each, the Hamming distance is defined as the number of differences
Exclusive OR can compute Hamming Distance
  Example:
  The XOR of the two strings is
  110 + 011 = 101 => 2
  d(000, 001) = 1, d(000, 101) = 2
  d(101,100) = 1, d(001, 010) = 2

## Slide 18: Hamming Distance cont’
When errors transform a valid codeword into another valid codeword
  Use of Hamming distance
Consider Figure 8.6 that lists the four (4) possible datawords and Hamming distance
minimum Hamming distance, dmin
  Determines the number of bit errors that can cause such transformation

## Slide 19: Hamming Distance cont’

## Slide 20: The Tradeoff Between Error Detection and Overhead
A large value of dmin is desirable
  fewer than dmin bits are changed -> error(s) occurred
the maximum number of bit errors, e, can be computed as:
A code with a higher value of dmin sends more redundant information than an error code with a lower value of dmin
Code rate R can be computed as:

## Slide 21: Minimum Hamming Distance
The minimum Hamming distance for a code, D(min), determines its error detecting and error correcting capability.
For any code word, X, to be interpreted as a different valid code word, Y, at least D(min) single-bit errors must occur in X.
Thus, to detect k (or fewer) single-bit errors, the code must have a Hamming distance of D(min) = k + 1.

## Slide 22: Minimum Hamming Distance cont’
Hamming codes can detect D(min) - 1 errors and correct errors
Thus, a Hamming distance of 2k + 1 is required to be able to correct k errors in any data word.
Hamming distance is provided by adding a suitable number of parity bits to a data word.
The minimum number of redundant (parity) bits
  (n+1) * 2m , m: data bits, r: redundant bits
  n = m + r

## Slide 23: Error correction with Row and Column (RAC) parity
1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
A RAC encoding allows a receiver to correct any single bit error
And to detect errors in which two or three bits are changed.

## Slide 24: Error correction with Row and Column (RAC) parity cont’
The two disagreements correspond to the row and column position of the error
  Correct the error
RAC can correct any single data error
When two or three bits are changed
  RAC encoding detects an odd number of errors only

## Slide 25: Alternative Error Detection Schemes
Many alternative schemes that:
  Detect multi-bit errors
  Correct errors through redundant information
Checksum and CRC are two widely used techniques

## Slide 26: Checksum
Idea
Sender | Receiver
Adds the given number e.g. number (5, 12, 11, 9) Sum = 37 | Adds the received numbers and compares the result with the sum
The sum is sent in addition to the list of numbers e.g. (5, 12, 11, 9, 37) | If the two are the same, assume no error, else data are not accepted

## Slide 27: Checksum con’t
If the sender sends negative (complement) of the sum, the computation would be easy
  E.g. sends (5, 12, 11, 9, -37)
The receiver simply adds all the numbers including the checksum.
If the result is 0, no error is assumed
else data is discarded.

## Slide 28: Checksums
Sum of data in message treated as array of integers
  Can be 8-, 16- or 32-bit integers
  Typically use 1’s-complement arithmetic
  Example - 16-bit checksum with 1’s complement arithmetic
  The size and easy of computation => requires addition only

## Slide 29: Limitations to checksums
May not catch all errors

## Slide 30: Cyclic Redundancy Checks
Detect more errors without increasing additional info in each packet
Consider data in message as coefficients of a polynomial
Divide that coefficient set by a known polynomial e.g. 1011
Example: 1010 = x3 + x (known polynomial)  y
  Preprocessing: data bits: m
  1. add k zeros to the data  m + k  n
  2. divide n with y
  3. find remainder  r
  4. subtract remainder from n  z
Transmit remainder as CRC
No error if z is divisible by y at the receiver
Easy to implement in hardware

## Slide 31: Cyclic Redundancy Checks
Key Properties
  Arbitrary Length Message
  Excellent Error Detection
  Fast Hardware Implementation

## Slide 32
Modulo 2 arithmetic works like clock arithmetic.
In clock arithmetic, if we add 2 hours to 11:00, we get 1:00.
In modulo 2 arithmetic if we add 1 to 1, we get 0. The addition rules couldn’t be simpler:
0 + 0 = 0 0 + 1 = 1
1 + 0 = 1 1 + 1 = 0
Cyclic Redundancy Checks

## Slide 33
Find the quotient and remainder when 1111101 is divided by 1101 in modulo 2 arithmetic.
  As with traditional division, we note that the dividend is divisible once by the divisor.
  We place the divisor under the dividend and perform modulo 2 subtraction.
Cyclic Redundancy Checks

## Slide 34
Find the quotient and remainder when 1111101 is divided by 1101 in modulo 2 arithmetic…
  Now we bring down the next bit of the dividend.
  We see that 00101 is not divisible by 1101. So we place a zero in the quotient.
Cyclic Redundancy Checks

## Slide 35
Find the quotient and remainder when 1111101 is divided by 1101 in modulo 2 arithmetic…
  We find the quotient is 1011, and the remainder is 0010.
This procedure is very useful to us in calculating CRC syndromes.
Note: The divisor in this example corresponds to a modulo 2 polynomial: X 3 + X 2 + 1.
Cyclic Redundancy Checks

## Slide 36
Suppose we want to transmit the information string: 1111101.
The receiver and sender decide to use the (arbitrary) polynomial pattern, 1101.
The information string is shifted left by one position less than the number of positions in the divisor.
The remainder is found through modulo 2 division (at right) and added to the information string: 1111101000 + 111 = 1111101111.
Cyclic Redundancy Checks

## Slide 37
If no bits are lost or corrupted, dividing the received information string by the agreed upon pattern will give a remainder of zero.
We see this is so in the calculation at the right.
Real applications use longer polynomials to cover larger information strings.
  Some of the standard polynomials are listed in the next slide
Cyclic Redundancy Checks

## Slide 38: Most commonly used CRC Polynomials
CRC-8: 100000111 (9 bits)
CRC-10: 11000110011
CRC-12: 1100000001111
CRC-16: 11000000000000101
CRC-CCITT: 10001000000100001
CRC-32: 100000100110000010001110110110111
CRC-64

## Slide 39: Hardware Components in CRC
XOR
Shift register

## Slide 40: CRC Hardware
K bit shift register -> degree of polynomial
An example that computes 16-bit CRC

## Slide 41: Error Detection and Frames
Error detection typically done for each frame
Error in frame typically causes receiver to discard frame
Example - CRC sent after end of frame computed on data in frame