## Slide 1: Local Area Networks: Packets, Frames, and Topologies

## Slide 2: Circuit Switching
Circuit switching
  Creates a path between sender and receiver
  Guaranteed isolation between paths
  Circuit switching networks use electronic devices to establish circuits
  multiple circuits are multiplexed over shared media
    the result is known as a virtual circuit
    Improving reliability and reducing the chances of packet reordering or loss
Telephone technology uses circuit switching
  They offer a dedicated connection between two telephones

## Slide 3: Circuit Switching

## Slide 4: Circuit Switching
Three general properties:
  Point-to-point communication
  Three-steps:
    circuit creation, use, and termination
    switched or permanent
  Performance equivalent to an isolated physical path
    Established communication not affected by other
    circuit switching must provide the illusion of an isolated path

## Slide 5: Packet Switching
A packet switching system uses statistical multiplexing
  multiple sources compete for the use of shared media

## Slide 6: Packet Switching
each message divided into packets
  Variable size
  maximum packet size for each packet-switching technology
Arbitrary, asynchronous communication
  allows one-to-many communication
  communication can occur at any time
No set-up required
  system always in ready to deliver state
  No need to notify termination
Performance varies
  due to statistical multiplexing among packets
  multiplexing occurs among packets

## Slide 7: Packet Switching
Advantage: low cost due to resource sharing
To provide communication among N computers
  With a circuit-switched network
    at least N/2 independent paths
  With packet switching, a network must have
    Only one connection for each computer

## Slide 8: Local and Wide Area Packet Networks
Packet switching technologies classified by the distance
  Short distance costs less (e.g., inside a single building)
  Long distances more expensive (e.g., across several cities)

## Slide 9: Standards for Packet Format and Identification
Each packet must have the identification of the intended recipient
Must agree on how to identify a recipient and where to place the identification in a packet
Standards organizations
  Institute for Electrical and Electronic Engineers (IEEE)
In 1980, IEEE organized the Project 802 LAN/MAN Standards Committee to produce standards for networking

## Slide 10: Standards for Packet Format and Identification
IEEE covers the lower two layers of the protocol
Figure 13.4 gives an illustration of a protocol as viewed by various standards organizations, such as
  Institute for Electrical and Electronic Engineers (IEEE)
  World Wide Web Consortium (W3C)
  Internet Engineering Task Force (IETF)

## Slide 11: Standards for Packet Format and Identification

## Slide 12: IEEE 802 Model and Standards
IEEE divides Layer 2 of the protocol stack into two conceptual sub-layers, as Figure 13.5 (below) illustrates
  The Logical Link Control (LLC)
    Provides flow control, error detection (use of checksum and CRC) to the frames, multiplexing, and addressing between higher and lower layers
    Supports multiple network protocols by adding LLC headers and using service access points (DSAP and SSAP) – which network protocol the frame belongs to
  The Media Access Control (MAC)
    sublayer specifies how multiple computers share underlying medium

## Slide 13: IEEE 802 Model and Standards
IEEE assigns a multi-part identifier of the form XXX.YYY.ZZZ
  XXX denotes the category of the standard
  YYY denotes a subcategory
IEEE has many working groups
  Each working group consists of representatives from the industrial and academic communities
  IEEE allows a working group to remain active provided the group makes progress and the technology is still deemed important
  If a technology under investigation is no longer relevant, the group can decide to disband

## Slide 14
Figure 13.6
Examples of the identifiers IEEE has assigned to various LAN
standards
802.11ac (Wi-Fi 5)
5GHz, up to 3.5Gbps
MU-MIMO, 256-QAM

## Slide 15
Standard | Frequency Band | Max Speed | Main Features | Use Cases
802.11ax (Wi-Fi 6/6E) - 2019 | 2.4 GHz, 5 GHz, 6 GHz (6E) | 9.6 Gbps | OFDMA, MU-MIMO, 1024-QAM, BSS Coloring, TWT | IoT, smart homes, high-density environments
802.11be (Wi-Fi 7) | 2.4 GHz, 5 GHz, 6 GHz | 46 Gbps (theoretical) | 320 MHz channels, 4K-QAM, Multi-Link Operation | AR/VR, 8K streaming, enterprise environments
802.11ad (WiGig) | 60 GHz | 7 Gbps | High-speed, short-range, ideal for point-to-point communication | Wireless VR, HD media streaming, docking stations
802.11ay | 60 GHz | 176 Gbps (theoretical) | Enhanced range and speed over 802.11ad | 8K streaming, wireless data centers, VR
802.11ah (HaLow) | Sub-1 GHz (900 MHz) | 347 Mbps | Low power, long-range, IoT-focused | IoT, smart cities, industrial automation
802.11af (White-Fi) | TV White Spaces | 568 Mbps | Long-range, uses TV broadcast frequencies | Rural broadband, smart agriculture, IoT
Summary of Key Wi-Fi Standards:

## Slide 16: Point-to-Point and Multi-Access Networks
LAN technologies are for sharing
  any computer on the LAN can communicate with any other
  A LAN is a multi-access network
  fair use of a network
LAN technologies can provide direct connection among communicating entities
LANs connect computers along with peripheral devices

## Slide 17: LAN Topologies
Many LAN technologies exist
Each network is classified into a category according to its topology or general shape
This section describes four basic topologies that are used to construct
  13.8.1 Bus Topology
  13.8.2 Ring Topology
  13.8.3 Mesh Topology
  13.8.4 Star Topology
  Tree topology – scalable & flexible but root node failure disrupts the network
  Hybrid topology – combination of topologies, flexible, complex design and management

## Slide 18: LAN Topologies
Tree

## Slide 19: LAN Topologies Bus Topology
Bus topology usually consists of a single cable to which computers attach
The ends of a bus network must be terminated
  to prevent electrical signals from reflecting back along the bus
Any computer attached to a bus can send on the cable
  and all computers receive the signal
Because all computers attach directly to the cable
  any computer can send data to any other computer
The computers attached to a bus network must coordinate
  to ensure that only one computer sends a signal at any time

## Slide 20: LAN Topologies Ring Topology
Ring topology arranges for computers to be connected in a closed loop
  name ring arises because one can imagine the computers and the Ring topology requires a computer to connect to a small device that forms the ring
  this is needed for the ring to continue operation even if some of the computers are disconnected

## Slide 21: LAN Topologies Mesh Topology
A network that uses a mesh topology provides a direct connection between each pair of computers
The chief disadvantage of a mesh arises from the cost:
  A mesh network connecting n computers requires:
  The important point is that the number of connections needed for a mesh network grows faster than the number of computers
Because connections are expensive
  few LANs employ a mesh topology in special circumstances

## Slide 22: LAN Topologies Star Topology
In star topology, all computers attach to a central point
The center of a star network is often called a hub
A typical hub
  accepts data from a sending computer and delivers it to the appropriate destination
Star networks seldom have a symmetric shape
  a hub often resides in a location separate from the computers attached to it
For example, computers can be in offices, while the hub resides in a location where general access is not allowed

## Slide 23: LAN Topologies The Reason for Multiple Topologies
A ring makes it easy for computers to coordinate access and to detect whether the network is operating correctly
  One cut in the connection may disable entire network
A star helps protect the network from damage to a single cable because each cable connects only one machine
A bus requires fewer wires than a star, but has the same disadvantage as a ring

## Slide 24: Summary Table of LAN Topologies
Topology | Description | Advantages | Disadvantages
Star | Central hub connects all devices | Easy to manage; failure of one device doesn't affect others | Central hub failure affects entire network
Bus | All devices on a single cable | Cost-effective; easy to install | Failure of main cable disrupts the network
Ring | Devices in a circular connection | Predictable transmission times | A single device or cable failure disrupts the network
Mesh | Multiple interconnections between devices | High redundancy and reliability | Expensive and complex to manage
Tree | Hierarchical structure | Scalable and easy to manage | Root node failure disrupts the network
Hybrid | Combination of topologies | Flexible and adaptable | Complex design and management

## Slide 25: Packet Identification, Demultiplexing, MAC Addresses
IEEE has created a standard for addressing
Consider packets traversing a shared medium as Figure 13.2 (below) illustrates

## Slide 26: Packet Identification, Demultiplexing, MAC Addresses
Each packet has a specific recipient
  only the intended recipient should process the packet
Demultiplexing uses an identifier known as an address
Each computer is assigned a unique address
Each address consists of 48 bits; IEEE uses the term Media Access Control address (or simply MAC address)
  Same as Ethernet address
IEEE allocates a unique address for each piece of interface
  Each Network Interface Card (NIC) contains a unique IEEE address

## Slide 27: Packet Identification, Demultiplexing, MAC Addresses
IEEE assigns a block of addresses to each vendor
  allows the vendor to assign a unique value to each device
  there is a 3-byte Organizationally Unique ID (OUI)
    OUI identifies the equipment vendor
    a 3-byte block that identifies a particular NIC

## Slide 28: Unicast, Broadcast, and Multicast Addresses
The IEEE addressing supports three types of addresses

## Slide 29: Unicast, Broadcast, and Multicast Addresses
the IEEE address format reserves a bit to distinguish between unicast and multicast
  Nothing for a broadcast address
broadcast address consists of 48 bits that are all 1s
  a broadcast address has the multicast bit set
Broadcast can be viewed as a special form of multicast
  Each multicast address corresponds to a group of computers
  Multicast addressing can be used in the link layer, such as Ethernet multicast, and the Internet layer for IP V4 and IP V6
  Broadcast address corresponds to a group that includes all computers on the network

## Slide 30: Broadcast, Multicast, and Efficient Multi-Point Delivery
Broadcast and multicast addresses permit efficient delivery to many computers
the efficiency comes from a shared medium
In a typical LAN
  each computer on the LAN monitors the shared medium
  extracts a copy of each packet and determines the address
  determine whether the packet should be processed or ignored
Algorithm 13.1 gives the algorithm a computer uses to process packets

## Slide 31: Broadcast, Multicast, and Efficient Multi-Point Delivery

## Slide 32: Frame delivery
FFFFFFFFFFFF
06-23-4c-f9-11-b4
06-23-4c-65-d1-f7
06-23-4c-13-f2-43
06-23-4c-f9-3d-23
FFFFFFFFFFFF
FFFFFFFFFFFF
FFFFFFFFFFFF
MAC address: 06-23-4c-f9-11-b4
06-23-4c-f9-11-b4
06-23-4c-f9-11-b4
06-23-4c-13-f2-43
06-23-4c-f9-11-b4
06-23-4c-13-f2-43
For the listing of IEEE multicast address: http://standards.ieee.org/develop/regauth/grpmac/public.html

## Slide 33: Frames and Framing
Framing
  the structure added to a sequence of bits or bytes that allows a sender and receiver to agree on the exact format of the message
In a packet-switched network, each frame corresponds to a packet
A frame consists of two conceptual parts:
  Header that contains metadata, such as an address
    Information used to process the frame
  Payload that contains the data being sent
    The message being sent

## Slide 34: Frames and Framing
A message is opaque
  The network only examines the frame header
  The payload only meaningful to the sender and receiver
Some technologies delineate each frame by sending a short prelude before the frame and a short postlude after it

## Slide 35: Frames and Framing
Assume that a packet header consists of 6 bytes
  the payload consists of an arbitrary number of bytes
We can use ASCII character set to specify:
  Beginning: the Start Of Header (SOH) character
  End: the End Of Transmission (EOT) character

## Slide 36: Byte and Bit Stuffing
In the ASCII character set
  SOH has hexadecimal value 201
  EOT has the hexadecimal value 204
An important question arises
  what happens if the payload of a frame includes one or more bytes with value 201 or 204?
The answer lies in a technique known as byte stuffing
  that allows transmission of arbitrary data without confusion

## Slide 37: Byte and Bit Stuffing
To distinguish data from control information
  Sender replaces each control byte with a sequence
  Receiver replaces the sequence with the original one
  the underlying system never confuses data with control information
Known as byte stuffing
  the terms data stuffing and character stuffing are sometimes used
A related technique used with systems that transfer a bit stream is known as bit stuffing

## Slide 38: Byte and Bit Stuffing
SOH and EOT must not appear in the payload (reserved)
Byte stuffing reserves a third character to represent reserved characters in the data
  E.g., the ASCII character ESC may be used as the third character
  Each occurrence of the reserved <- replaced by two character sequence
One possible mapping can be:

## Slide 39: Byte and Bit Stuffing
As the figure specifies
  the sender replaces each occurrence of SOH by the two characters ESC + A
  each occurrence of EOT by the characters ESC + B
  and each occurrence of ESC by the two characters ESC + C
A receiver reverses the mapping
  by looking for ESC followed by one of A, B, or C and replacing the 2-character combination with the appropriate single character
Figure 13.13 shows an example payload and the same payload after byte stuffing has occurred
  Note that once byte stuffing has been performed, neither SOH nor EOT appears anywhere in the payload

## Slide 40: Byte and Bit Stuffing

## Slide 41: Bit stuffing
Not to confused with control signals
Maintains synchronization: Prevent long sequences of the same bit value
Inserting extra, non-informational bits into the data stream to prevent misunderstanding, e.g., after 5 consecutive 1, insert one zero. Then the receiver removes it