## Slide 1: Multiplexing and Demultiplexing
COSC350

## Slide 2: Multiplexing Concepts
Typically, two communicating stations will not utilize the full capacity of a data link
For efficiency, it should be possible to share that capacity
Such sharing is called multiplexing
Multiplexing to refer to the combination of information streams from multiple sources for transmission over a shared medium
Demultiplexing to refer to the separation of a combination back into separate information streams

## Slide 3: Multiplexing Concepts cont’

## Slide 4: Multiplexing Concepts cont’
Multiple signals with data can be carried on the same medium without interference
  Allows multiple simultaneous data streams
  Dialup modems can carry full-duplex data on one voice channel
Example: multiple TV stations in air medium
Each separate signal is called channel

## Slide 6: Types of Multiplexing
Major approaches
  Frequency Division Multiplexing (FDM)
  Orthogonal FDM (OFDM) : 4G/5G, Wi-Fi
  Wavelength Division Multiplexing (WDM)
  Time Division Multiplexing (TDM)
  Code Division Multiplexing (CDM)
TDM supports legacy systems and telephony infrastructure
FDM is still widely used
WDM is a form of FDM used for optical fiber
CDM/CDMA is a mathematical approach used in cell phone mechanisms

## Slide 7: Frequency Division Multiplexing
The most familiar method to anyone who ever used radio or television set – widely used, long-lived
Can be used with analog signals
  Each carrier is assigned a separate channel
Modulation equipment is needed
  move each signal to the required frequency band
Multiplexing equipment is needed
  combine the modulated signals
Modulated signal requires a certain bandwidth called channel

## Slide 9: FDM cont’
Each communicating pair gets a private transmission path
some limitations in FDM
  interference may occur if channels are too close
  demultiplexer must divide the signal into separate carriers
  FCC in USA regulates adequate spacing
  Carrier frequencies must have a guard band
Figures 11.4 and 11.5 show an example
  200 KHz allocated to each of 6 channels with a guard band of 20 KHz

## Slide 12: Range of Frequencies Per Channel
FDM susceptible to noise and distortion
Most FDM systems assign each sender and receiver pair a range of frequencies
FDM can choose how the frequencies are used
Two primary ways:
  Increase the data rate
  Increase immunity to interference
To increase the overall data rate
  a sender divides the frequency range of the channel into K carriers
  sends 1/K of the data over each carrier

## Slide 13: Range of Frequencies Per Channel
A sender can perform FDM within an allocated channel
To increase immunity to interference
  spread spectrum
basic idea
  Divide the channel into K carriers
  transmit the same data over multiple channels
  a receiver choose one with fewest errors
Works well in noisy environment

## Slide 14: Hierarchical FDM
FDM hardware can shift frequencies
A set of incoming signals with the range between 0 and 4 KHz
  leave the first stage as is
  the second onto the range 4 KHz to 8 KHz
  the third onto the range 8 KHz to 12 KHz, and so on
Hierarchy in FDM multiplexors is that each maps its inputs to a larger, continuous band of frequencies
Figure 11.6 illustrates the concept of hierarchical FDM

## Slide 16: Orthogonal Frequency-Division Multiplexing
Application areas:
  Digital television/audio broadcasting
  DSL internet access
  Wireless networks
  4G/5G
A type of digital transmission
How it works:
  Incoming bitstream is divided into multiple streams
  Multiple bits transmitted in parallel with overlapping spectra using multiple orthogonal subcarriers
  Subcarriers are orthogonally arranged to avoid interferences
  Fast Fourier transformation algorithm is used for demodulation

## Slide 17: Wavelength Division Multiplexing
A variation of FDM for fiber optic channels
Wavelength of light is used for multiplexing
Uses prism or diffraction grating to separate channels
Potentially many channels (hundreds) can be multiplexed together over long-haul routes
Example: DWDM: assign each source a specific wavelength (channel) and transmit all the lambdas on the same fiber optic (some successful configurations)
  320 channels with 2.5Gbps (800 Gbps)
  160 channels with 10Gbps (1.6 Tbps)
  128 channels with 40Gbps (5.12 Tbps)
  96 channels with 400Gbps (38Tbps)

## Slide 19: Time Division Multiplexing (TDM)
TDM does not rely on special properties of electromagnetic energy
  multiplexing in time simply means transmitting an item from one source, then transmitting an item from another source, and so on

## Slide 20: Synchronous Time Division Multiplexing
Can be used with digital signals or analog signals carrying digital data
When the achievable data rate of the medium exceeds the data rate of digital signals to be transmitted
Data from various sources are carried in repetitive frames and each frame consists of a set of time slots. Time slots are pre-assigned
The slot length equals to the transmitter buffer length, typically a bit or a character.
Items are sent in a round-robin fashion

## Slide 21: Framing in TDM (Telephone System)
Multiplex digital streams from multiple phone calls
  the specific form of TDM used to multiplex digital telephone calls
The phone system TDM
  to insure that a demultiplexor stays synchronized with the multiplexor
Why synchronization?
  Each slot doesn’t have any indication of the output
A demultiplexor cannot tell where a slot begins
  a slight difference in the clocks can cause misinterpretation

## Slide 22: Framing in TDM (Telephone System)
To prevent misinterpretation, an extra framing channel is used as input
A single bit is inserted as a framing bit
A demultiplexor extracts data from the framing channel and checks for alternating 0 and 1 bits
If an error causes a demultiplexor to lose a bit
  Upon detecting an error -> allow the transmission to be restarted
Figure 11.10 illustrates the use of framing bits

## Slide 24: Hierarchical TDM
TDM hierarchy uses N times the bit rate
  In FDM, each successive stage uses N times the frequencies
Additional framing bits are added to the data
  the bit rate of each successive layer of hierarchy is slightly greater than the aggregate voice traffic
Compare the example TDM hierarchy
  in Figure 11.11 with the FDM example in Figure 11.6

## Slide 26: How to calculate T1 speed
T1 connections have 24 voice channels (24 DS0)
PCM takes 8000 samples per second
  Each sample is represented by 8 bits (1 byte)
1 sample from 24 voice circuits would be 24 * 8 bits => 192 bits
  All the samples will be placed into a frame
  There will be 1 framing bit added in order to prevent misinterpretation
T1 transmits 8000 samples per second
  8000 * 193bits => 1.544Mbps

## Slide 27: Unfilled Slots with Synchronous TDM
Synchronous TDM works with uniform rate
Many sources generate data in bursts, with idle time between bursts
in Figure 11.12
  sources on the left produce data items at random
  the synchronous multiplexor leaves a slot unfilled
In practice, a slot cannot be empty
  Empty slot is assigned a value (such as zero)
  an extra bit is used to indicate invalid value

## Slide 29: Statistical Time Division Multiplexing
In synchronous TDM, many of the time slots in a frame a usually wasted.
Assumption for this method is that the data rate of the output is less than the sum of the data rates of the inputs.
User data are buffered and transmitted as rapidly as possible using available time slots.
Address information is required to assure proper delivery.

## Slide 30: Statistical Time Division Multiplexing cont’

## Slide 31: Statistical Time Division Multiplexing cont’
Statistical multiplexing incurs extra overhead
Consider demultiplexing:
  In a synchronous TDM system a demultiplexor knows that every N slot corresponds to a given receiver
  In a statistical multiplexing system, the data in a given slot can correspond to any receiver
Each slot must contain the identification of the receiver to which the data is being sent
Later chapters discuss identification mechanisms
  that are used with statistical multiplexing in packet switching networks and the Internet

## Slide 32: Inverse Multiplexing
Consider two points with multiple transmission media
  no single medium’s bit rate is sufficient
To solve the problem, multiplexing is used in reverse
  spread a high-speed digital input over multiple lower-speed circuits for transmission and combine the results at the receiving end

## Slide 33: Inverse Multiplexing

## Slide 34: Inverse Multiplexing
An inverse multiplexor requires special hardware
  the sender and receiver agree on how data arriving from the input will be distributed over the lower-speed connections
  Different delay may cause out of order arrival
  the system must insure that the order is preserved
Despite its complexity, inverse multiplexing is widely used in the Internet

## Slide 35: Code Division Multiplexing (CDM)
Several channels simultaneously share the same
Used in some cellular telephone system and some satellite communication
Cellular telephone version is called Code Division Multi-Access (CDMA)
  When CDM is used to allow multiple users to share a single communications channel
  Another important application of CDMA is the GPS

## Slide 36: CDM (or spread spectrum)
Each sender is assigned a unique binary code Ci
  that is known as a chip sequence
  chip sequences are selected to be orthogonal vectors
  (dot product of any two sequences are zero, e.g., UV = 0)
CDM doesn’t rely on physical properties but on values from orthogonal vector spaces

## Slide 37: CDM (or spread spectrum) cont’
At any point in time, each sender has a value to transmit, Vi
  The senders each multiply Ci x Vi and transmit the results
Simultaneous transmission
  the values are added together
  over the same frequency band
To extract value Vi, a receiver multiplies the sum by Ci
  Ex: c1v1, c2v2 -> c1v1+ c2v2 (transmission)
  -> (c1v1+ c2v2 ) * c1(extraction of v1)

## Slide 38: CDM

## Slide 39: CDM
The first step consists of converting the binary values into vectors that use -1 to represent 0:
If we think of the resulting values as a sequence of signal strengths to be transmitted at the same time
  the resulting signal will be the sum of the two signals

## Slide 40: CDM
A receiver treats the sequence as a vector
  computes the product of the vector and the chip sequence
  treats the result as a sequence, and converts the result to binary by interpreting positive values as binary 1 and negative values as 0
Thus, receiver number 1 computes:
Interpreting the result as a sequence produces: (2 -2 2 -2)
  which becomes the binary value: (1 0 1 0)
  note that 1010 is the correct value of V1
  receiver 2 will extract V2 from the same transmission