## Slide 1: Transmission Modes
COSC350

## Slide 2: A Taxonomy of Transmission Modes
The way data is sent over the underlying medium
  Serial: one bit is sent at a time
  Parallel: multiple bits are sent at the same time

## Slide 3: Parallel Transmission
Transfer data bits at the same time over separate media
Used with a wired medium that uses multiple, independent wires
The signals on all wires are synchronized
Advantages
  High speed: it can send N bits at the same time
  Match to underlying hardware

## Slide 5: Serial Transmission
One bit at a time
Advantages
  Can be extended with much less cost
  No timing problem: only one wire
  No electromagnetic noise at high data rate
To use serial communication
  Convert between parallel form to the serial form used on the wire
  Simple case:
    A single chip known as Universal Asynchronous Receiver and Transmitter (UART) for conversion

## Slide 7: Transmission order: Bits and Bytes
MSB or LSB first?
  Little-endian: LSB first
  Big-endian: MSB first
  Sender and receiver must agree
MSB and LSB can be used together
  Byte: big-endian, bit: little-endian
  E.g. 87654321 16 15 14 13 12 11 10 9 …..

## Slide 9: Universal Serial Bus
An industry standard developed in the mid-1990s
Designed to standardize the connection of computer peripherals to personal computers
Effectively replaced a variety of earlier interfaces such as serial and parallel ports, as well as power chargers for portable devices
The most recent USB specification is USB4 Version 2.0, which offers a significant bandwidth upgrade of up to 80 Gbps.

## Slide 10: Universal Serial Bus
Up to 80Gbps (USB4. V2)
External GPU, 3D rendering,
VR, AR, enterprise edge computing
and cloud computing

## Slide 11: Timing of Serial Transmission
Three categories:
  Asynchronous transmission can occur at any time
  Synchronous transmission occurs continuously with no gap between the transmission of two data items
  Isochronous transmission occurs at regular intervals with a fixed gap

## Slide 12: Encoding details
Several standard organizations specify the details:
  IEEE
  ITU
  EIA
To be interoperable network hardware should conform to the standards

## Slide 13: The RS-232C Standard
Example use
  Connection to keyboard/mouse
  Serial port on PC
Specified by EIA
Voltage is +15 or –15
Cable limited to < 50 feet
Uses asynchronous communication

## Slide 15: Asynchronous communication
Sender and receiver must agree on
  Number of bits per character
  Duration of each bit
Receiver
  Does not know when a character will arrive
  May wait forever
To ensure meaningful exchange send
  Start bit before character
  One or more stop bits after character

## Slide 16: Synchronous Transmission
A synchronous mechanism transmits
  back-to-back transmission
The sender and receiver must remain synchronized
RS-232 requires an extra start bit and stop bit
  Requires 10 bit times
On a synchronous system
  each character is sent without start or stop bits

## Slide 18: Duration of a bit in RS-232C
Determined by baud rate
  Typical baud rate is 9.6Kbaud, 14.4Kbaud, 28.8Kbaud
  Duration of bit is 1/baud_rate
Sender and receiver must agree on the details
Receiver examines signal
Disagreement results in framing error

## Slide 19: Bytes, Blocks, and Frames
When sender sends bits continually with synchronous mechanism
  Use of framing:
    Frame is used in a synchronous mechanism to handle a block of bytes
  For proper synchronization
    a frame starts with a special sequence of bits
  When no data to send
    an idle sequence (or idle byte)

## Slide 21: Isochronous Transmission
Isochronous transmission
  Provides steady bit flow for multimedia applications
Reasoning for steady bit flow
  To prevent jitter
At a fixed rate, R
  Network interface handles transmission at exactly R bits per second

## Slide 22: Simplex, Half-Duplex, and Full-Duplex Transmission
Type of communications channel:
  Simplex
  Full-Duplex
  Half-Duplex
Simplex: transfer data in a single direction
  analogous to broadcast radio or television
Full-Duplex: allows transmission in two directions simultaneously
  analogous to a voice telephone conversation

## Slide 24: Simplex, Half-Duplex, and Full-Duplex Transmission
Half-Duplex: A half-duplex mechanism involves a shared transmission medium
  The shared medium can be used for communication in each direction but not simultaneously
  It is analogous to using walkie-talkies

## Slide 25: Two-way communication
Desirable in practice
Require each side to have transmitter and receiver
Called full-duplex
Transmitter on one side connected to receiver on other
Separate wires needed to carry current in each direction
Common ground wire
DB-25 connector (RS-232 defines it) used
  Pin 2 is transmit
  Pin 3 is receive

## Slide 26: DCE and DTE Equipment
Terms Data Communications Equipment (DCE) and Data Terminal Equipment (DTE) - originally from AT&T
  Communication equipment (circuit-terminating equipment)
  DTE typically represents computers, terminals, or devices that originate or process data
  DCE refers to devices like modems, routers, or network interfaces that provide a connection between DTE and a communication line e.g. modem <-> phone line
When a business leases a data circuit from a phone company
  the phone company installs DCE equipment
  the business attaches DTE equipment to the DCE equipment

## Slide 27: DCE and DTE Equipment
Several standards for the interface between DCE and DTE
  The RS-232 standard: lower than 20Kbps
  the RS-449 standard: 2Mbps
  The RS-485 standard: 10Mbps, up to 4000ft, half/full duplex
  The RS-422 standard: 10Mbps, up to 4000ft, full duplex