## Slide 1: The IEEE MAC Sub-Layer

## Slide 2: Introduction
Multiple, independent computers must coordinate to access a shared medium
Three approaches:
  Modified form of Multiplexing
  Controlled access
  Random access

## Slide 3
Fig. 14.1
A Taxonomy of Mechanisms for Multi-Access

## Slide 4: Channel Allocation
A mapping between a given communication and a channel in the underlying transmission system
Static Channel Allocation
  Fixed frequency for a set of communicating entities
Dynamic Channel Allocation
  A set of entities using the network varies over time: e.g. cellphone

## Slide 5: Channelization Protocols
FDMA: Frequency Division Multi-Access
  Extension of FDM
  Allow independent stations to choose carrier frequencies
TDMA: Time Division Multi-Access
  Extension of TDM
  Time slice is allocated dynamically – first come first serve
CDMA: Code Division Multi-Access

## Slide 6: Controlled Access Protocols
Polling: Use of centralized controller
  Round Robin Order
  Priority Order: e.g. higher order for IP phone than PC
Reservation: submit a request for the next round
  Often used with satellite transmission
  Form a list of stations and allow them to transmit
Toke Passing: stations circulate a token

## Slide 7: Random Access Protocols
ALOHA: historic protocol used in an early radio network; not used in real networks
  Use of inbound and outbound frequencies in ALOHAnet
CSMA/CD:
  Basis for Ethernet; most widely used
CSMA/CA:
  Basis for Wi-Fi wireless networks

## Slide 8: Random Access Protocols - ALOHA

## Slide 9: ALOHA
When transmitting:
  it transmits the packet on the inbound frequency
  the central transmitter repeats the transmission on the outbound frequency (which all stations can receive)
Checking transmission
  listens to the outbound channel
    if a copy of its packet arrives, moves to the next packet
    if no copy arrives, waits a short time and tries again

## Slide 10
Interference may cause transmission failure
  simultaneously transmission cause collision
    The transmissions will be garbled
The protocol handles a collision
  by requiring a sender to retransmit each lost packet

## Slide 11: CSMA(Carrier Sense Multiple Access)
  No central control managing when computers transmit on ether
  Ethernet employs CSMA to coordinate transmission among multiple attached computers
  Carrier Sense with Multiple Access
    Multiple access - multiple computers are attached and any can be transmitter
    Carrier sense - computer wanting to transmit tests ether for carrier before transmitting

## Slide 12: Collision detection – CD (IEEE 802.3)
  Even with CSMA, two computers may transmit simultaneously
    3 states are possible – contention, transmit, idle
      Contention period is twice the time that the signal travels 2 farthest stations
    Both check ether at the same time, find it idle, and begin transmitting
    Window for transmission depends on speed of propagation in ether

## Slide 13: Collision detection – CD (IEEE 802.3)
  Signals from two computers will interfere with each other
  Overlapping frames is called a collision
    No harm to hardware
    Data from both frames is garbled
    Send out collision presence signal

## Slide 14: Ethernet CD
Ethernet interfaces include hardware to detect transmission
Monitors outgoing signal
Garbled signal is interpreted as a collision
After collision is detected, computer stops transmitting

## Slide 15: Recovery from collision
Computer that detects a collision sends special signal to force all other interfaces to detect collision
Computer then waits for Ether to be idle before transmitting
If both computers wait same length of time, frames will collide again
Standard specifies maximum delay, and both computers choose random delay less than maximum

## Slide 16: Recovery from collision
After waiting, computers use carrier sense to avoid subsequent collision
  Computer with shorter delay will go first
  Other computers may transmit first

## Slide 17: Binary Exponential backoff
  Even with random delays, collisions may occur
  Especially likely with busy segments
  Computers double delay with each subsequent collision
  Reduces likelihood of sequence of collisions
  After i collisions, a random number between 0 and 2i –1 is chosen
    K * 51.2 μs, where k is the random number between 0 and 2i – 1
    When i = 3, k is between 0 and 23 - 1

## Slide 18: Limited connectivity with wireless
In contrast with wired LAN, not all participants may be able to reach each other
Low signal strength
Propagation blocked by walls, etc.
  Can't depend on CD; not all participants may hear
Wireless LANs use a modified access protocol known as CSMA with Collision Avoidance (CSMA/CA)

## Slide 19: CSMA/CA
For computer 1, computer 3 may not be visible. So when computer 1 and computer 3 transmit at the same time to computer 2, it will detect a collision. It is called the “hidden station” problem.

## Slide 20: CSMA/CA
Wireless uses collision avoidance rather than collision
detection
Transmitting computer sends very short message to receiver
Receiver responds with short message reserving slot for transmitter
Response from receiver is broadcast so all potential transmitters receive reservation

## Slide 21: CSMA/CA

## Slide 22: Collisions
  Receiver may receive simultaneous requests
    Results in collision at receiver
    Both requests are lost
    Neither transmitter receives reservation; both use backoff and retry
  Receiver may receive closely spaced requests
    Selects one
    Selected transmitter sends message
    Transmitter not selected uses backoff and retries