## Slide 1: COSC 290 (Lab) #5
Amaizu Gabriel
gamaizu1@students.towson.edu

## Slide 2: Circuit Design Tutorial

## Slide 3: How to design a logical circuit
Algorithm
Truth table
Boolean Expression
Circuit Drawing
Karnaugh
Map

## Slide 4: 1) Algorithm Establishment
On the computer programmer’s perspective
  boolean input1, input2;
  scanf (%d, &input1);
  scanf (%d, &input2);
  if(input1 == input2)
    System.out.println(“output (same)\n”);
  else
    System.out.println(“(different)\n”);

## Slide 5: 1) Algorithm Establishment (cont)
On the circuit designer’s perspective
  Take two inputs  1-bit each
    Output 1 if the same
    Output 0 if different

## Slide 6: 2) Truth Table Construction
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 7: 3) Karnaugh map
Developed by Maurice Karnaugh in 1953
Description
  Transformation of a truth table to extract a boolean expression
Method
  Sum of products (Positive logic: e.g., and )
  Product of sums (Negative logic: e.g., and )
How to build the Karnaugh map
  One-on-one relationship between a Karnaugh map and an output
    E.g., 3 outputs  3 Karnaugh maps needed
  Conversion to the 2-dimentional graph; X- and Y-axis construction
    Categorize inputs to two groups
  Placement of outputs to the appropriate cases
    Copy outputs from a truth table to its Karnaugh map
  The extraction of Boolean expression (Positive logic applied)
    Make a product from each output position if its value is 1 and sum all the products.
Note
  The output positions can be grouped with the number of

## Slide 8: 3) Karnaugh map (cont)
Boolean expression
  Truth table
  Boolean expression
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 | A |  | 
B |  | 0 | 1
 | 0 | 1 | 0
 | 1 | 0 | 1

## Slide 9: 3) Karnaugh map to Boolean Expression
Rules
  Adjacent 1s in the K-map represents opportunities to simplify the expression
  The minterms for the final expression are found by encircling groups of 1s in the map
  Minterm groups must be rectangular and must have an area that is power of 2 (i.e., 1,2,4,8..)
  Min term rectangles should be as large as possible without containing any 0s
  Groups may overlap in order to make each one larger

## Slide 10: 4) Boolean Expression Extraction
Boolean expression
  Sum of Products (Positive logic: e.g., 1=A & 0=)
Boolean expressions  Electric circuit diagrams
 | B |  | 
A |  | 0 | 1
 | 0 | 1 | 0
 | 1 | 0 | 1

## Slide 11: 5) Draw the circuit!

## Slide 12: 4) Boolean Expression Extraction
Examples
  Sum of Products (Positive logic: e.g., 1=A & 0=)
 | B |  | 
A |  | 0 | 1
 | 0 | 1 | 1
 | 1 | 1 | 1
A B | 00 01 |  | 11 | 10
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0

## Slide 13: Practical Example

## Slide 14: Let’s think
Build a 1-bit binary adder
  0 + 0 = 0
  0 + 1 = 1
  1 + 0 = 1
  1 + 1 = 0 and a carry

## Slide 15: Let’s think (cont)
We have two 1-bit binary values for addition:
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
 | B |  | 
A |  | 0 | 1
 | 0 | 0 | 1
 | 1 | 1 | 0
 | B |  | 
A |  | 0 | 1
 | 0 | 0 | 0
 | 1 | 0 | 1
S (sum)
C (Carry-out)

## Slide 16: Half Adder
Add two one-bit binary numbers.
INPUT |  | OUTPUT | 
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
<Truth Table>
 | A |  | 
B |  | 0 | 1
 | 0 | 0 | 1
 | 1 | 1 | 0
<Karnaugh Map>
 | A |  | 
B |  | 0 | 1
 | 0 | 0 | 0
 | 1 | 0 | 1

## Slide 17
Binary Decoder in Digital Logical
An n-to-m decoder converts inputs into output with multiple bit inputs resulting in 2^n outputs.
The decoder works by producing all possible outputs of 2^n depending on if the input is on or off, producing only one positive output for each unique combination of inputs.

## Slide 18
Binary Decoder in Digital Logical