## Slide 1: COSC 290 (Lab) #7
Amaizu Gabriel
gamaizu1@students.towson.edu

## Slide 2: Error-checking method
Data transmission
  Do you want to save your data?
    Yes(1) / No(0)
      S: 1  R: 0
      S: 1  R: 1
Types of Error-checking
  Detection
    Checking whether the received data bits has an error
      Parity check
  Correction
    Checking which data bit is erroneous + correction!
      Hamming code

## Slide 3: Parity-checking method
Idea
  Count the number of 1s and adjust it to odd or even by a parity bit
Types for parity-checking
  Method
    Odd
      Make the number of 1s odd with a parity bit (Odd: correct, Even: incorrect)
    Even
      Make the number of 1s even with a parity bit (Even: correct, Odd: incorrect)
Data bits | Parity bit | 
 | odd | even
1001011 | 1 | 0
0101010 | 0 | 1
0010101 | 0 | 1

## Slide 4: Parity-checking method (cont)
Full functions
  Parity Generator
    Generate a parity bit corresponding to the chosen method, even or odd.
  Parity Checker
    Result: 1  no error, 0  error
Parity Generator
Parity
Checker
Sender
Receiver
Data bits
Data bits + 1-bit parity
Request the message again.

## Slide 5: Parity-checking method (cont)
Example of even parity checking method
  S: 11011  R: 11011 (Done)
  S: 11011  R: 11001 (Resend)
  S: 11011  R: 10111 (Done)
Note
  Parity checking method is used to detect 1-bit binary error.
  It could not find errors with 2n bits (n=1, 2, 3,…).

## Slide 6: Parity Generator
Truth table
1st bit | 2nd bit | EVEN parity bit | ODD parity bit
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 7: Parity Generator (cont)
Boolean expressions
01 (data bits) + 1 (even parity bit)
00 (data bits) + 1 (odd parity bit)
INPUT1 | INPUT2 | XOR’s OUTPUT | XNOR’s OUTPUT
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 8: Faults on Parity Generator
A XOR gate w/ 3 inputs

## Slide 9: XOR Investigation (cont)
3-input XOR (built in Logisim)

## Slide 10: XOR Investigation (cont)
3-input XOR (a chain of 2-input XORs)

## Slide 11: Faults on Parity Generator (cont)
A XOR gate w/ 3 inputs
XOR gates w/ 3 inputs,
a chain of 2-input XORs

## Slide 12: Faults on Parity Generator (cont)

## Slide 13: Faults on Parity Generator (cont)

## Slide 14: Parity Checker
Caution
  1: No error, 0: Error
    * logisim

## Slide 15: Hamming code 7-4
Parity bits | Data bits | Total bits | Name | Data rate
2 | 1 | 3 | Hamming(3,1) | 
3 | 4 | 7 | Hamming(7,4) | 
4 | 11 | 15 | Hamming(15,11) | 
5 | 26 | 31 | Hamming(31,26) | 
n |  |  | Hamming(T, D) | D/T
Parity bits | Data bits | Total bits | Name | Data rate
2 | 1 | 3 | Hamming(3,1) | 
3 | 4 | 7 | Hamming(7,4) | 
4 | 11 | 15 | Hamming(15,11) | 
5 | 26 | 31 | Hamming(31,26) | 
n |  |  | Hamming(T, D) | D/T
Invented by Richard Hamming in 1950
Idea
  Generate multiple parity bits to make a correction
Format

## Slide 16: Hamming code (cont)
How to generate Hamming code
1. Choose one of parity-generating methods.
EVEN or ODD

## Slide 17: Hamming code (cont)
Bit position | 7 | 6 | 5 | 4 | 3 | 2 | 1
How to generate Hamming code (cont)
2. Determine the total bits and draw the bit-positioning table.
EVEN

## Slide 18: Hamming code (cont)
EVEN
How to generate Hamming code (cont)
3. Convert each bit-position number into binary.
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Parity bit coverage |  | 1 |  |  |  |  |  |  | 
 |  | 2 |  |  |  |  |  |  | 
 |  | 4 |  |  |  |  |  |  | 
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Parity bit coverage |  | 1 |  |  |  |  |  |  | 
 |  | 2 |  |  |  |  |  |  | 
 |  | 4 |  |  |  |  |  |  | 

## Slide 19: Hamming code (cont)
EVEN
How to generate Hamming code (cont)
4. Make sure positions for parity bits.
Parity bit positions: th
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Parity bit coverage |  | 1 | 1 |  | 1 |  | 1 |  | 1
 |  | 2 | 1 | 1 |  |  | 1 | 1 | 
 |  | 4 | 1 | 1 | 1 | 1 |  |  | 
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Parity bit coverage |  | 1 | 1 |  | 1 |  | 1 |  | 1
 |  | 2 | 1 | 1 |  |  | 1 | 1 | 
 |  | 4 | 1 | 1 | 1 | 1 |  |  | 

## Slide 20: Hamming code (cont)
EVEN
How to generate Hamming code (cont)
5. Place data bits in the reverse order.
Hamming code position: th
  e.g., ,
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Code word |  |  | 0 | 1 | 0 |  | 1 |  | 
Parity bit coverage |  | 1 |  |  |  |  |  |  | X
 |  | 2 |  |  |  |  |  | X | 
 |  | 4 |  |  |  | X |  |  | 
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Code word |  |  | 0 | 1 | 0 |  | 1 |  | 
Parity bit coverage |  | 1 |  |  |  |  |  |  | X
 |  | 2 |  |  |  |  |  | X | 
 |  | 4 |  |  |  | X |  |  | 

## Slide 21: Hamming code (cont)
EVEN
How to generate Hamming code (cont)
6. Generate each parity bit on each place.
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Data bits |  |  | 0 | 1 | 0 | Z | 1 | Y | X
Parity bit coverage |  | 1 |  |  |  |  |  |  | 
 |  | 2 |  |  |  |  |  |  | 
 |  | 4 |  |  |  |  |  |  | 
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Data bits |  |  | 0 | 1 | 0 | Z | 1 | Y | X
Parity bit coverage |  | 1 |  |  |  |  |  |  | 
 |  | 2 |  |  |  |  |  |  | 
 |  | 4 |  |  |  |  |  |  | 
X, Y, and Z are binary numbers

## Slide 22: Hamming code (cont)
“EVEN”
How to generate Hamming code (cont)
7. Combine the calculated parity bits with data bits.
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Data bits |  |  | 0 | 1 | 0 | 1 | 1 | 0 | 1
Parity bit coverage |  | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
 |  | 2 | 1 | 1 | 0 | 0 | 1 | 1 | 0
 |  | 4 | 1 | 1 | 1 | 1 | 0 | 0 | 0
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1
Data bits |  |  | 0 | 1 | 0 | 1 | 1 | 0 | 1
Parity bit coverage |  | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
 |  | 2 | 1 | 1 | 0 | 0 | 1 | 1 | 0
 |  | 4 | 1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 23: Hamming code (cont)
How to detect an error
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | R
Data bit |  |  | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 
Parity bit coverage |  | 1 | 0 |  | 0 |  | 1 |  | 1 | 
 |  | 2 | 0 | 1 |  |  | 1 | 0 |  | 
 |  | 4 | 0 | 1 | 0 | 1 |  |  |  | 
Hamming code |  |  | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 
Received code |  |  | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 
Detect the error |  | 1 | 0 |  | 0 |  | 1 |  | 1 | 0
 |  | 2 | 0 | 1 |  |  | 1 | 1 |  | 1
 |  | 4 | 0 | 1 | 0 | 1 |  |  |  | 0
Bit position |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | R
Data bit |  |  | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 
Parity bit coverage |  | 1 | 0 |  | 0 |  | 1 |  | 1 | 
 |  | 2 | 0 | 1 |  |  | 1 | 0 |  | 
 |  | 4 | 0 | 1 | 0 | 1 |  |  |  | 
Hamming code |  |  | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 
Received code |  |  | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 
Detect the error |  | 1 | 0 |  | 0 |  | 1 |  | 1 | 0
 |  | 2 | 0 | 1 |  |  | 1 | 1 |  | 1
 |  | 4 | 0 | 1 | 0 | 1 |  |  |  | 0
[HC-generating process]
1. Choose a parity checking method
2. Determine total bits
3. List up position #s in binary
4. Make sure parity bits’ position
5. Place data bits on the table
6. Generate each parity bit
7. Combine parity bits with data
[HC-checking process]
1. Mimic 1 to 5 of above
2. Calculate parity bit for each place with R
3. Read all Rs in order
4. The number given by R is an error bit-position if it’s not 0 in binary.