## Slide 1: Modulation and Modems
COSC350

## Slide 2: 1. Introduction
•Fact: an oscillating signal travels farther than direct current
•For long-distance communication
–Send a sine wave (called a carrier wave)
–Change (modulate) the carrier to encode data
•The frequency of electromagnetic energy determines how the energy propagates
•Frequency of carrier fixed

## Slide 3: Analog Modulation Schemes
Modulation: changes made in a carrier
  according to the information being sent
Modulation takes two inputs
  a carrier
  a signal
fundamental characteristics of the wave must be changed to encode signal
primary techniques
  Amplitude modulation
  Frequency modulation
  Phase shift modulation

## Slide 5: Amplitude Modulation (AM)
AM manipulates the amplitude of a carrier
  Results in the changes in the amplitude of the wave
As it is seen from the figure 10.2:
  the amplitude (i.e., magnitude) of the sine wave is modified
  a time-domain graph shows a shape similar to the signal that was used

## Slide 7: Frequency Modulation (FM)
In FM, frequency changes according to the signal:
  For stronger signal, the carrier frequency increases
  For weaker signal, the carrier frequency decreases
FM is more difficult to visualize
  slight changes in frequency may not be clearly visible

## Slide 9: Phase Modulation (PM)
One property of sine wave is its phase,
  offset is used to represent reference time from beginning
Changes in phase are possible -> phase shift
phase shift after cycle k
  Slight delay between cycle k completion and next sine wave
  the delay resembles a change in frequency
PM: a special form of frequency modulation

## Slide 10: Amplitude Modulation and Shannon's Theorem
the amplitude of a carrier changes based on modulation index
modulated signal cannot be zero
Shannon's Theorem
  If noise is constant
    the signal-to-noise ratio will become zero if the signal approaches zero
To get high data rate
  the carrier wave must be near maximum
  the signal-to-noise ratio remains as large as possible

## Slide 11: Modulation, Digital Input, and Shift Keying
Digital schemes use discrete values
To distinguish between analog and digital modulation
  shift keying is used rather than modulation
similar to analog modulation
  digital shift keying has a fixed set instead of a continuum of possible values
  AM allows the amplitude of a carrier to vary by arbitrarily small amounts in response to a change in the signal
    amplitude shift keying uses a fixed set of possible amplitudes

## Slide 12
Figure 10.4 Illustration of
a carrier wave
a digital input signal
amplitude shift keying
frequency shift keying

## Slide 13: Phase Shift Keying (PSK)
Amplitude and frequency modulations require at least one cycle of a carrier wave to send a single bit
  With an exception of special encoding scheme
More bits encoded in a single cycle
  More bits can be sent per unit time
PSK changes the phase of the carrier wave abruptly
  called a phase shift

## Slide 14: Phase Shift Keying (PSK)
There are three (abrupt) phase changes
A phase shift is measured by the angle of the change
The leftmost portion of sine wave changes its phase by 180 degrees

## Slide 15: Phase Shift and a Constellation Diagram
Data encoding using phase shifts
  A sender and receiver agree on the number of bits per second
  no phase shift may denote logical 0 and presence of phase shift logical 1
Constellation diagram
  the exact assignment of data bits to specific phase changes
Many variations of PSK exist
  Binary Phase Shift Keying (BPSK) or 2-PSK in Fig. 10.6
  Notation of 2-PSK may represent two possible values

## Slide 17: More phase shift keying
More data rate
  Measure the amount a carrier shifted
  Can recognizes set of phase shifts
    each phase shift can represent specific values of data
A power of 2 possible shifts
  a sender can use bits of data to select among the shifts
4 possible phase shifts in fig. 10.7
  a sender can use 2-bits of data to select among the 4-possible shift values -> 4-PSK mechanism

## Slide 19: More PSK
In theory, it is possible to increase the data rate by increasing the range of phase shifts
Thus, a 16-PSK mechanism can send twice as many bits per second as a 4-PSK mechanism
Limiting factors: noise and distortion

## Slide 20: Quadrature Amplitude Modulation
Motivation: more data rate
Change two characteristics of a carrier at the same time
Combination of ASK and PSK
  Quadrature Amplitude Modulation (QAM) or Quadrature Amplitude Shift Keying (QASK)
QAM on a constellation diagram
  distance from the origin as a measure of amplitude
  Figure 10.8 shows 16QAM with dark gray areas indicating the amplitudes
  64QAM and 256QAM are typically used for digital cable television and cable modem applications.
  256QAM delivers up to 38Mbps, Wi Fi 5 uses 256QAM and Wi-Fi 6 uses 1014QAM
  4096QAM is used for high speed

## Slide 22: Modem Hardware for Modulation and Demodulation
Carrier and a sequence of bits
  Modulator
  Demodulator
Transmission of data requires a modulator and a demodulator
Most communication systems are full duplex

## Slide 23: Modem
Used for long-distance communication
•Contains separate circuitry for
–Modulation of outgoing signal
–Demodulation of incoming signal
•Separate wires carry signals in each direction
•Modulator on one modem connects to demodulator on other

## Slide 24: Optical and Radio Frequency Modems
Can be used with other media
  Radio Frequency (RF)
  optical fibers
A pair of RF modems over radio
A pair of optical modems over optical fibers
Regardless of media, the principle remains the same:
  modulates a carrier signal with data
  data is extracted from the modulated carrier

## Slide 25: Dialup Modems
Uses an audio tone
Uses data to modulate an audible carrier
Interior of a modern telephone system: digital
  The phone system digitizes the incoming audio
  Transports a digital form internally
  Converts the digitized version back to analog audio for delivery
  The receiving modem demodulates the analog carrier
  Extracts the original digital data

## Slide 26: Dialup Modems cont’
The use of analog and digital signals by dialup modems (embedded in a computer) shown below
internal modem / external modem

## Slide 27: QAM Applied to Dialup
QAM is used with dialup modems for maximized data rate
Available frequencies between 300 and 3300 Hz
the extremes may not be handled well
  use frequencies between 600 and 3000 Hz
  the available bandwidth becomes 2400 Hz
A QAM scheme can increase the data rate dramatically

## Slide 28: QAM Applied to Dialup

## Slide 29: V.32 and V.32bis Dialup Modems
Consider the V.32 and V.32bis standards
Figure 10.12 and 10.13 illustrate the QAM constellation for
  a V.32 modem: 32 combinations of ASK and PSK
    a data rate of 9600 bps in each direction
  a V.32bis modem: 128 combinations of ASK and PSK
    a data rate of 14,400 bps in each direction
Sophisticated signal analysis may be needed to reveal the minor change

## Slide 32: Bandwidth requirements trend

## Slide 33: Modem application - Cable networks
Cable networks nowadays provide combined TV and data service using hybrid fiber coax (HFC) cabling architecture
Trunk coaxial cable of legacy networks are replaced by fibers that terminate in fiber nodes
Homes are connected to fiber nodes through coaxial cables fitted with bidirectional amplifiers.
Traditional cable networks were targeted at TV distribution (one-way) and are not suited for 2-way data service – data upstream was provided by dial-up phone but proved not a viable solution.
Digital signaling, two-way amplifiers on coax cables and fiber trunks with greatly increased capacity were introduced in the course of upgrading. Two-way cable networks provide an ‘extended Ethernet’ network that can span up to 100 miles.

## Slide 34: Modem application - Cable networks cont’

## Slide 35: Cable modem
Cable networks employ data over cable service interface specification (DOCSIS) that covers physical layer and data link layer.
Cable modem termination system
Cable modem to
customer premise equipment
interface
Radio Frequency Interface

## Slide 36: Cable modem con’t
DOCSIS 3.0 (2006)
  Downstream data rate of 160Mbps or higher
    Channel bonding
    4 or more channels
    256 QAM => ~ 40Mbps
    8x256 QAM => ~320Mbps
  Upstream data rates of 120Mbps or higher
    64QAM => ~30Mbps
    4x64QAM => ~ 120Mbps

## Slide 37: Cable modem con’t
DOCSIS 4.0 (2020)
  Downstream data rate of 10Gbps
    Channel bonding
    4 or more channels
    4096 QAM
  Upstream data rates of 6Gbps