## Slide 1: Transmission Media
cosc350

## Slide 2: Introduction
transmission media, including wired, wireless, and optical media
taxonomy of media types
basic concepts of electromagnetic propagation
the effect of shielding with respect to interference and noise
the concept of capacity

## Slide 3: Guided and Unguided Transmission
Categorization of transmission media
Two approaches:
  By type of path
  By form of energy
Physical Media
  Guided (wired): copper wiring, optical fibers
  Unguided (wireless): radio

## Slide 4: A Taxonomy by Forms of Energy
The diagram shows how physical media can be classified according to the form of energy used to transmit data

## Slide 5: Background Radiation and Electrical Noise
Electrical current needs a complete circuit
  two wires to form a circuit: send and return
The simplest form of wiring
  a cable with two copper wires
Each wire needs plastic coating for insulation
The outer coating put two wires together for easy connection

## Slide 6: Background Radiation and Electrical Noise
Computer networks use an alternative form of wiring
Facts related to Noise
  Noise (Random electromagnetic radiation) may present in normal operation
  Random noise can interfere with signals
  Metal acts as a shield (may absorb noise)

## Slide 7: Twisted Pair Copper Wiring
Type of wiring
  Unshielded Twisted Pair (UTP)
    also known as twisted pair wiring
  Coaxial Cable
  Shielded Twisted Pair (STP)
Twisting two wires may help reduce noise as shown in Figure 7.2

## Slide 8: Twisted Pair Copper Wiring

## Slide 9: Twisted Pair Copper Wiring
When two wires are in parallel
  The distance to the source of electromagnetic radiation may differ
  Different amount of electromagnetic radiation

## Slide 10: Shielding: Coaxial Cable and Shielded Twisted Pair
Limitations on twisted pair wiring
  strong electrical noise
  high frequencies used for communication
Interference may occur
  on top of a fluorescent light fixture
Distinguishing valid signals from noise can be difficult

## Slide 11: Shielding: Coaxial Cable and Shielded Twisted Pair
Extra metal shielding wiring
  Coaxial cable (coax): the wiring has a thick metal shield formed from braided wires that completely surround a center (inner) wire that carries the signal
  A coaxial cable can stand electrical noise and high frequencies
    The shield provides a barrier to electromagnetic radiation

## Slide 12: Shielding: Coaxial Cable and Shielded Twisted Pair

## Slide 13: Shielding: Coaxial Cable and Shielded Twisted Pair
braided wire makes coaxial cable flexible
  One variation -> shielded twisted pair (STP)
    Thinner
    Flexible metal shield surrounding one or more twisted pairs of wires
    the shield contains metal foil

## Slide 14: Standards organizations
American National Standards Institute (ANSI)
Telecommunications Industry Association (TIA)
Electronic Industries Alliance (EIA)

## Slide 15: Categories of Twisted Pair Cable
CAT 8 fully shielded twisted pair - data center / 40 Gbps
High-performance network

## Slide 16: Media Using Light Energy and Optical Fibers
three forms of media
  Optical fibers: most widely used
  InfraRed transmission
  Point-to-point lasers
Each fiber consists of
  A thin strand of glass or
  transparent plastic encased in a plastic cover
An optical fiber for a single direction
  two-way communication -> two fibers

## Slide 17: Media Using Light Energy and Optical Fibers
Light can change direction
  the boundary between two substances
For a given pair of substances
  there exists a critical angle, θ
  If (the angle of incidence = the critical angle)
    travel along the boundary
  If (the angle of incidence < θ )
    refracted
  If (the angle > θ )
    reflected

## Slide 18: Media Using Light Energy and Optical Fibers

## Slide 19: Media Using Light Energy and Optical Fibers
Reflection is not perfect
  Reflection absorbs some energy
  A photon may take a zig-zag path
  Dispersion over time
  Dispersion is a serious problem for long optical fibers

## Slide 20: Media Using Light Energy and Optical Fibers

## Slide 21: Types of Fiber and Light Transmission
Three forms of optical fibers :
  Multimode, Step Index
    used when performance is unimportant
    reflect frequently, high dispersion
  Multimode, Graded Index
    increase density near the edge -> reduce reflection and lower dispersion
  Single Mode
    provides the least dispersion
    smaller diameter and properties that help reduce reflection
    used for long distances and higher bit rates

## Slide 22: Types of Fiber and Light Transmission
Single mode fiber: focus light
  can travel long distances without becoming dispersed
  Minimal dispersion could increase the bit rate
Transmission: LED or Injection Laser Diode (ILD)
Reception: photo-sensitive cell or photodiode
  LEDs and photo-sensitive cells
    short distances and slower bit rates
    common with multimode fiber;
  single mode fiber
    long distance with high bit rates
    requires ILDs and photodiodes

## Slide 23: Optical Fiber Compared to Copper Wiring
Comparison between Optical fiber and copper wiring
  Optical fiber
    immune to electrical noise
    higher bandwidth
    Travelling light does not attenuate as much as electrical signals traveling across copper
  Copper wiring
    less expensive
    Installation is easy
    Copper wires are less likely to break if accidentally pulled or bent

## Slide 24: Infrared (IR) Communication Technologies
IR (e.g. TV remote)
  a form of electromagnetic radiation
  behaves like visible light but not visible to a human eye
Disperses quickly
Can reflect from a smooth, hard surface
Any opaque object can block the signal
IR commonly used to connect to a nearby peripheral
The wireless aspect of infrared can be attractive for laptop computers

## Slide 25: Infrared (IR) Communication Technologies

## Slide 26: Point-to-Point Laser Communication
Requires line-of-sight
Laser follows line-of-sight
  the beam is only a few centimeters wide
  The sending and receiving equipment must be aligned
  Used for outdoors and offers great distances
  useful in cities to transmit from building to building

## Slide 27: Electromagnetic (Radio) Communication
Most common form of unguided communication
  Radio Frequency (RF) range
RF energy
  Traverse long distances
  Penetrate solid objects
The properties depend on the frequency
Regulating Organization
  Federal Communications Commission (FCC) sets rules for how frequencies

## Slide 28: Electromagnetic (Radio) Communication
RF range (3KHz – 300GHz)

## Slide 29: Signal Propagation

## Slide 30
NASA

## Slide 31: Signal Propagation
two broad categories as in wireless comm.:
  Terrestrial
  Non-terrestrial
Frequency and amount of power used can affect:
  The speed
  The maximum distance
  Characteristics (penetrate solid object?)

## Slide 32: Types of Satellites
The laws of physics (specifically Kepler's Law) applied to a satellite, that orbits the earth
The orbital period depends on the distance from the earth
three broad categories
  LEO, MEO, GEO

## Slide 33
Types of Satellites

## Slide 34: GEO Communication Satellites
GEO
  the orbital period is the same as the earth
If positioned above the equator
  a GEO satellite remains in one position
A stationary satellite position
  Once aligned the equipment never needs to move

## Slide 35: GEO Communication Satellites

## Slide 36: GEO Communication Satellites
The distance required for a geostationary orbit is 35,785 kilometers or 22,236 miles
  which is approximately one tenth the distance to the moon
Time to travel to GEO satellite
A delay of approximately 0.2 seconds can be significant for some applications

## Slide 37: GEO Coverage of the Earth
How many GEO communication satellites are possible?
There is a limited amount of “space” available in the geosynchronous orbit above the equator
  Frequency separation to avoid interference
  the minimum separation depends on the power of the transmitters
However, as technology is evolving it’s possible to allocate more satellites in orbit

## Slide 38: GEO Coverage of the Earth
*Drawn to scale

## Slide 39: Low Earth Orbit (LEO) Satellites and Clusters
Low Earth Orbit (LEO)
  up to 2000 Km typically at altitudes of 500-600 kilometers or higher (above atmosphere)
  short delays (typically 1 to 4 ms)
The disadvantage of LEO
  the orbit does not match the rotation of the earth
From an observer's point of view on the earth
  an LEO satellite appears to move across the sky
    Needs rotating antenna to track the satellite
  Tracking is difficult because satellites move rapidly
  The orbit between 90 minutes and several hours depends on altitude

## Slide 40: Low Earth Orbit (LEO) Satellites and Clusters
LEO satellites used in clustering or in array deployment
  Communicate each other
For example,
Same group

## Slide 41: Tradeoffs Among Media Types
The choice of medium is complex
Choice involves the evaluation of multiple factors, such as:
  Cost
    materials, installation, operation, and maintenance
  Data rate
    number of bits per second that can be sent
  Delay
    time required for signal propagation or processing
  Affect on signal
    attenuation and distortion
  Environment
    susceptibility to interference and electrical noise
  Security
    susceptibility to eavesdropping

## Slide 42: Measuring Transmission Media
The two measures of performance for medium:
  Propagation delay
    the time required for a signal to traverse the medium
  Channel capacity
    the maximum data rate that the medium can support
Nyquist Theorem
  The relationship between the bandwidth of a transmission system and its capacity to transfer data
  Defines the maximum data rate without considering the effect of noise
  K possible signal levels, analog bandwidth B, the maximum data rate in bits per second, D,

## Slide 43: The Effect of Noise on Communication
Nyquist's Theorem cannot be achieved in practice due to electrical noise
Claude Shannon extended Nyquist's work to specify the maximum data rate with noise
  Shannon's Theorem
  where
    C is the effective limit on the channel capacity in bits per second
    B is the hardware bandwidth
    S/N is the signal-to-noise ratio, the ratio of the average signal power divided by the average noise power

## Slide 44: The Effect of Noise on Communication
Consider a transmission medium:
  a bandwidth of 1 KHz (typical wi-fi is 20MHz, linear SNR is 1000)
  an average signal power of 70 units
  an average noise power of 10 units
The channel capacity is:
The signal-to-noise ratio is often given in decibels (abbreviated dB), where a decibel is defined as a measure of the difference between two power levels
Figure 7.14 illustrates the measurement

## Slide 45: The Effect of Noise on Communication

## Slide 46: The Effect of Noise on Communication
the difference is expressed in decibels, defined as follows:
Using dB as a measure has two interesting advantages:
  First, it can give us a quick idea about outcome of an operations:
    a negative dB value: attenuated
    a positive dB value: amplified
  Second, if a communication system has multiple parts arranged in a sequence
    The dB measures of the parts can be summed to produce a measure of the overall system

## Slide 47: The Effect of Noise on Communication
Example:
  The voice telephone system:
    S/N approximately 30 dB
    an analog bandwidth of approximately 3000 Hz
  To convert signal-to-noise ratio dB into a simple fraction
    divide by 10 and use the result as a power of 10
    (i.e., 30/10 = 3, and 103 = 1000, so the signal-to-noise ratio is 1000)
  Shannon's Theorem applied to the telephone network:
  or approximately 30,000 bps
S/N dominates data rate

## Slide 48: The Significance of Channel Capacity
Nyquist's work
  Showed possibility of improving data rate with encoding technique
Shannon's Theorem
  Showed fundamental limit on date rate in a real communication system -> the laws of physics