## Slide 1: Extending LANs: Fiber Modems, Repeaters, Bridges, and Switches

## Slide 2: Introduction
LAN provides services from the link layer
  Node-to-node communication
  Framing: each frame has physical address
  Link access: MAC protocol handles transport over the link
  Reliable delivery: normally not provided
  Flow control: limited at data link layer
  Error detection/ correction
  Half-duplex/ full duplex

## Slide 3: Introduction cont’
LAN technologies are designed with constraints of speed, distance and costs
Typical LAN technology can span, at most, a few hundred meters
Factors considered when designing a network technology:
  Capacity
  Max delay
  distance

## Slide 4: LAN design for distance
Many LANs use shared medium
Length of medium affects fair, shared access to medium
CSMA/CD - delay between frames, minimum frame length
Length of medium affects strength of electrical signals and noise immunity

## Slide 5: LAN extensions
Several techniques extend diameter of LAN medium
Most techniques use additional hardware
LAN signals relayed between LAN segments
Resulting mixed technology stays within original engineering constraints while spanning greater distance

## Slide 6: Fiber optic extensions
The simplest LAN extension mechanism:
  an optical fiber and a pair of fiber modems
  connect a computer to a remote Ethernet

## Slide 7: Fiber optic extensions cont’
Fiber modems:
    accept packets over the Ethernet interface and send them over the optical fiber
    accept packets that arrive over the optical fiber and send them over the Ethernet interface
Typically connect two LANs in different buildings through a bridge

## Slide 8: Connecting Devices
Connecting
Devices
Networking
Devices
Internetworking
Devices
Repeaters
(physical)
Gateways
(Network and above)
Routers
(Network)
Bridges
(Data Link)

## Slide 9: Repeaters
A repeater:
  an analog device used to propagate LAN signals over long distances
  does not understand packets or signal coding
  amplifies the signal received
Cable box
repeater
Remote
sensor
((((((
Infrared transmitted
to Cable box

## Slide 10: Bridges
Connect two LAN segments
Retransmit frames from one segment on other segment(s)
Handle complete frame
  Recognize not only the signal but also the address of each frame
  Perform some processing on frames
Invisible to other attached computers

## Slide 11: Bridged LAN segments
Relatively easy to use - just plug in
Isolate collisions, noise

## Slide 12: Filtering bridges
Bridges can do additional processing
  Don't forward collisions, noise
  Only forward frames where necessary
frame filtering
  Uses MAC addresses to perform filtering
  Learns location of stations by watching frames
  Forwards all broadcast and multicast packets

## Slide 13: Frame filtering
Bridge checks destination of each incoming frame
Looks up destination in list of known stations
  Forwards frame to next interface on path to destination
  Doesn't forward frame if destination on LAN segment from which frame was received

## Slide 14: How does bridge set up table?
Bridge examines source address in each frame
Adds entry to list for LAN segment from which frame was received
Must forward any frame whose destination is not in the list on every interface

## Slide 15: Filtering example

## Slide 16: Startup behavior of filtering bridges
Initially, the forwarding tables in all bridges are empty
First frame from each station on LAN is forwarded to all LAN segments
After all stations have been identified, frames are only forwarded as needed
May result in burst of traffic after, e.g., power failure

## Slide 17: Designing with filtering bridges
Filtering bridge allows concurrent use of different LAN segments if traffic is local
U and V can exchange frames at the same time X and Y exchange frames
Designers identify patterns of local communication and isolate groups of communicating computers with bridges

## Slide 18: Bridges and cycles
  Four LAN segments currently connected by three bridges and a fourth bridge about to be inserted

## Slide 19: Bridges and cycles cont’
the fourth bridge
  creates a loop
The loop forwards broadcasts indefinitely
  Creates broadcast flooding
Distributed Spanning Tree (DST)
  Create a tree to prevent a cycle

## Slide 20: Distributed Spanning Tree
Initially (DEC in 1985) designed for Ethernet networks
  Spanning Tree Protocol (STP)
STP consists of three steps:
  Root election
  Shortest path computation
  Forwarding
Ethernet bridges communicate amongst themselves using a multicast address that is reserved for STP

## Slide 21: Distributed Spanning Tree
IEEE created a standard named 802.1d (in 1990)
IEEE standard 802.1q
  provides a way to run STP on a set of logically independent networks
  share a physical medium
Cisco created Per-VLAN Spanning Tree (PVST) for use on a VLAN switch
IEEE standard 802.1w introduced the Rapid STP (RSTP) has been incorporated in 801.1d-2004 (in 1998), and now replaces STP, some versions are
  Multiple Instance STP (MISTP)
  Multiple STP (MSTP)

## Slide 22: Switching and Layer 2 Switches
An Ethernet switch (a Layer 2 switch)
  a switch provides multiple ports
  a switch allows computers to send frames to one another
The difference between a hub and a switch:
  a hub operates as an analog device that forwards signals among computers
  a switch is a digital device that forwards packets
  a hub as simulating a shared transmission medium
  a switch as simulating a bridged network

## Slide 24: Switches and hubs
A switch consists of an intelligent interface attached to each port
  a central fabric that provides simultaneous transfers
An interface contains
  A processor, memory, and other hardware needed to accept a packet
  A forwarding table
An interface can buffer arriving packets when an output port is busy
Advantage of using a switched LAN
  a hub can only support one transmission at a time
  a switch permits multiple transfers to occur at the same time, provided the transfers are independent

## Slide 26: Switched Ethernet
Contention moved from bus to “single point”
Ethernet switch emulates CSMA/CD
Upon buffer overflow => collision signal
Medium-haul GigE/10GigE (802.3ae): 500m, 5km, 40km
  Disable CSMA/CD
  Purely point-to-point link
QoS: IEEE 802.3p
Today’s Ethernet: switch, CSMA/CD, short- and long-distance LAN -> a result of incremental legacy-respecting changes

## Slide 27: VLAN Switches
Allows a manager to configure a single switch to emulate multiple, independent switches using VLAN tag (defined as 802.1Q by IEEE)
A set of ports on the switch can be specified as virtual LAN 1 and so on
When a computer on virtual LAN 2 broadcasts a packet
  only those computers on the virtual LAN 2 receive a copy
An Ethernet frame with an 802.1Q VLAN tag

## Slide 28: VLAN Switches
It is important to guarantee that a set of computers can communicate
For example, a company may choose to provide a firewall between computers in the CEO's office and other computers in the company
E.g. computers A, C, F can be assigned as VLAN 1
802.1Q format used
VLAN
switch 1
VLAN
switch 2
D E F
Regular Ethernet frames are used